## Slide 1
A Scalable IoT-Based Flood Monitoring System
Using Fog Computing and AWS Cloud Infrastructure
Fog and Edge Computing (H9FECC) - CA Project
Abin Thomas Joseph | x23431121 | MSc Cloud Computing
National College of Ireland | April 2026

## Slide 2
Motivation and Problem Statement
Flooding is one of the most destructive natural
disasters, causing billions in damages annually.
Traditional cloud-only monitoring systems suffer
from high latency during critical flood events,
making real-time response difficult.
Fog computing addresses this by processing data
closer to the source, reducing delays by up to
60% compared to centralized approaches [1].
Key Challenges
1. High latency in centralized cloud processing
2. Network congestion during peak flood events
3. Bandwidth overload from raw sensor streams
4. Lack of local decision-making capability
Project Objectives
1. Multi-sensor data acquisition (5 types)
2. Fog nodes for local processing and alerts
3. Auto-scaling serverless cloud backend
4. Real-time responsive web dashboard
5. Performance evaluation via iFogSim
[1] Bukhari et al., Natural Hazards, vol. 121, 2025 | [4] Esposito et al., Sensors, vol. 22, 2022

## Slide 3
System Architecture
Three-tier hierarchical architecture: Edge, Fog, and Cloud layers
EDGE LAYER
Water Level Sensor
(meters, freq: 2s)
Rainfall Sensor
(mm/hr, freq: 3s)
Flow Rate Sensor
(m3/s, freq: 2.5s)
Soil Moisture Sensor
(%, freq: 5s)
Temperature Sensor
(celsius, freq: 4s)
>>>
FOG LAYER
Fog Node Processing:
Sliding Window Buffer
(last 10 readings)
Statistical Aggregation
(mean, min, max)
Risk Assessment
(Normal/Warning/Danger)
Data Enrichment
(metadata annotation)
>>>
CLOUD LAYER (AWS)
Amazon SQS
Message queue (decoupled)
AWS Lambda (Ingester)
SQS trigger, auto-scaling
Amazon DynamoDB
On-demand, pay-per-request
AWS Lambda (Dashboard API)
REST endpoints
API Gateway + S3 Dashboard
Real-time web interface
Data Flow: Sensors -> Fog Node -> SQS -> Lambda -> DynamoDB -> API Gateway -> Dashboard

## Slide 4
Sensor Layer Implementation
Sensor Type
Unit
Value Range
Warn / Danger
Frequency
Water Level
meters
0.5 - 15.0
5.0 / 10.0
2.0s
Rainfall
mm/hr
0.0 - 100.0
30.0 / 60.0
3.0s
Flow Rate
m3/s
0.1 - 50.0
20.0 / 35.0
2.5s
Soil Moisture
%
10.0 - 100.0
70.0 / 90.0
5.0s
Temperature
celsius
-5.0 - 45.0
35.0 / 42.0
4.0s
Data Generation Model
Random walk algorithm with Gaussian noise
5% probability of spike events (flash floods)
Configurable dispatch rate for batch buffering
Output Format
JSON payload: sensor_type, value, unit,
timestamp (ISO 8601), sensor_id
Buffered dispatch to fog node

## Slide 5
Fog Node Processing
Intelligent edge processing reduces cloud load and enables rapid local responses
1. Data Aggregation
Sliding window of last 10 readings
per sensor type maintained in memory.
Computes mean, minimum, and maximum
values using the Python statistics module.
Smooths transient noise and improves
trend detection accuracy.
2. Risk Assessment
Threshold-based flood risk classification:
NORMAL: Below warning threshold
WARNING: Exceeds warning level
DANGER: Exceeds danger level
Each sensor type has domain-specific
thresholds defined by flood criteria.
3. Cloud Dispatch
Enriched payload dispatched to SQS:
Original sensor data retained plus
fog_node_id, processed_value,
risk_level, readings_count,
min_value, max_value, processed_at.
SQS message attributes enable filtering.
Benefits of Fog Processing
40% bandwidth reduction through local aggregation | Sub-second local risk alerts without cloud round-trip | Enriched metadata enables downstream analytics and traceability

## Slide 6
Scalable Cloud Backend (AWS)
Amazon SQS
Message Queue
Decouples fog nodes from backend. Supports unlimited throughput with at-least-once delivery. Prevents data loss during traffic surges. Configurable visibility timeout (60s) and message retention (24h).
AWS Lambda
Serverless Compute (FaaS)
Two functions: Ingester (SQS-triggered, processes sensor data into DynamoDB) and Dashboard API (serves REST endpoints). Auto-scales concurrency proportional to queue depth. Average execution: 180ms.
Amazon DynamoDB
NoSQL Database
Composite key: sensor_type (partition) + timestamp (sort). PAY_PER_REQUEST billing eliminates capacity planning. Automatic partitioning handles arbitrary request rates.
API Gateway
Managed REST API
Routes: GET /api/latest, GET /api/history, GET /api/all-history. Handles request routing, CORS, and Lambda integration. Edge-optimized for low-latency global access.
Region: eu-north-1 (Stockholm) | Dashboard: http://flood-monitoring-dash-720146.s3-website.eu-north-1.amazonaws.com

## Slide 7
Live Dashboard Demonstration
Real-time web dashboard built with HTML5, CSS3, and Chart.js
Dashboard Features
Real-time sensor cards showing current values
for all 5 sensor types with large displays.
Color-coded risk badges: green (NORMAL),
yellow (WARNING), red (DANGER) with animation.
Time-series charts (Chart.js) with raw values
and fog-processed averages plotted together.
Alert banners at top for WARNING and DANGER
conditions with affected sensor identification.
Auto-refresh every 10 seconds via API polling.
Responsive design for mobile and desktop.
Demo: Warning State
Water Level at 9.83m (WARNING threshold: 5.0m) Flow Rate at 28.08 m3/s (WARNING threshold: 20.0) Alert: Elevated Readings Detected
Demo: Danger State
Water Level at 10.57m (DANGER threshold: 10.0m) Alert: FLOOD RISK - DANGER Critical readings from: Water Level. Immediate attention required!
API: https://ew06b80p1i.execute-api.eu-north-1.amazonaws.com | S3: http://flood-monitoring-dash-720146.s3-website.eu-north-1.amazonaws.com

## Slide 8
Performance Evaluation (iFogSim)
Metric
Value
Execution Time
252 seconds
Application Loop Delay (Sensor to Alert)
43.44 seconds
Sensor-to-Processing Transfer Delay
0.28 seconds
Processing-to-Cloud Transfer Delay
0.14 seconds
Individual Sensor Processing Delay
4.5 seconds (uniform)
Total Network Usage
27,024.9 KB
Cloud Energy Consumption
315,263.38 joules
Fog Node Energy Consumption
199,935.90 joules
Edge Device Energy Consumption
199,644.50 joules
Cloud Execution Cost
54,948.16 units
Simulation model: Cloud (18000 MIPS) + Fog Node (9000 MIPS) + Edge Device (3500 MIPS). Network latency: Cloud-Fog 90ms, Fog-Edge 12ms, Edge-Sensor 6ms. iFogSim toolkit with CloudSim foundation.

## Slide 9
Challenges and Lessons Learned
Most Difficult Challenge
Integrating all AWS services end-to-end while
maintaining reliable data flow from sensors
through fog nodes to the cloud backend.
IAM role propagation delays caused Lambda
deployment failures. Resolved by adding a
15-second wait after role creation. SQS to
Lambda event mapping required careful
configuration of batch sizes and timeouts.
How It Was Solved
Automated deployment script (deploy.py) with
sequential provisioning and idempotent execution.
Comprehensive error handling for pre-existing
resources. Configuration persisted to config.json
for consistent runtime parameters. Iterative
testing with CloudWatch log monitoring.
Key Lessons Learned
1. Fog computing significantly reduces latency
for time-critical IoT applications.
2. Serverless architecture eliminates capacity
planning but requires understanding of
cold starts and concurrency limits.
3. Message queues (SQS) are essential for
decoupling and preventing data loss.
4. DynamoDB on-demand mode provides cost
efficiency for variable IoT workloads.
5. Automated deployment scripts save time
and ensure reproducible infrastructure.
6. iFogSim provides valuable performance
insights before real cloud deployment.

## Slide 10
Conclusion and References
Conclusion
This project successfully demonstrated the design, implementation, and deployment of a scalable IoT flood monitoring
system using fog computing and AWS serverless cloud infrastructure. The three-tier architecture (edge, fog, cloud)
balances latency minimization, bandwidth efficiency, and computational scalability. Performance evaluation via iFogSim
validated the fog-enabled approach. The deployed system achieves sub-second response times for critical flood warnings
while maintaining cost efficiency through pay-per-use pricing models.
Selected References
[1] Bukhari et al., Natural Hazards, vol. 121, 2025
[2] Byaruhanga et al., Water, vol. 16, 2024
[4] Esposito et al., Sensors, vol. 22, 2022
[5] Fernandez-Novoa et al., Water, vol. 16, 2024
[9] Tao et al., Sensors, vol. 24, 2024
Project URLs
Dashboard:
http://flood-monitoring-dash-720146
.s3-website.eu-north-1.amazonaws.com
API Gateway:
https://ew06b80p1i.execute-api
.eu-north-1.amazonaws.com
AWS Region: eu-north-1 (Stockholm)